AF Fine Tuning Lens Identification
Prepared 2007-12-31 (149/109444) by Bill Claff

All Nikon CPU lenses contain a "chip" and that chip has both a lens ID and chip ID.
Both of these IDs are unique between Nikon lenses.

Non-Nikon CPU lenses reuse Nikon lens and chip IDs.

The AF Fine Tuning feature appears to use either the lens ID or chip ID to identify the lens; and this will work perfectly with Nikon lenses.

However, if you have any non-Nikon lenses that conflict with a Nikon lens that you own, or you have multiple non-Nikon lenses with the same IDs; then you will have a conflict since you can only save one set of AF Fine Tuning values per ID.

One serious overuse of an ID occurs with the following group of Sigma lenses that all have the same lens and chip IDs as the 300mm f/2.8D ED-IF AF-S Nikkor:

- 10-20mm F4-5.6 EX DC HSM

- 12-24mm F4.5-5.6 EX DG ASPHERICAL HSM

- 14mm F2.8 EX ASPHERICAL HSM

- 17-35mm f2.8-4 EX ASPHERICAL HSM

- 30mm F1.4 EX DC HSM

- 50-500mm F4-6.3 EX RF HSM

- 70-200mm F2.8 EX HSM

- 100-300mm F4 EX IF HSM APO

- 120-300mm F2.8 EX DG IF HSM APO

- 150mm F2.8 EX DG HSM APO MACRO

- 180mm F3.5 EX (DG) APO Macro IF HSM

- 300mm F2.8 EX DG APO HSM

- 300-800mm F5.6 EX DG HSM APO

I have confirmed this behavior with my Sigma 30mm and Sigma 100-300mm lenses.

Nikon could make the firmware "smarter" and have it use other information such as focal length in addition to the ID but they have no motivation to help non-Nikon lens manufacturers.

BTW, once an ID is in use by AF Fine Tuning it remembers the focal length and aperture information until that lens is removed from the list.

Here's another set of lenses that would appear identical to each other:

- 8mm F4 EX Circular fisheye

- 15mm F2.8 EX DIAGONAL fisheye

- 15-30mm F3.5-4.5 EX DG ASPHERICAL

- 17-35mm F2.8-4 EX DG ASPHERICAL HSM

- 18-50mm F2.8 EX DC

- 18-50mm F3.5-5.6 DC

- 18-125mm F3.5-5.6 DC

- 18-200mm F3.5-6.3 DC

- 20mm F1.8 EX DG ASPHERICAL RF

- 24mm F1.8 EX DG ASPHERICAL MACRO

- 24-60mm F2.8 EX DG

- 24-70mm F2.8 EX DG MACRO

- 24-70mm F3.5-5.6 ASPHERICAL HF

- 24-135mm F2.8-4.5 Aspherical IF

- 28mm F1.8 EX Aspherical DG DF MACRO

- 28-70mm F2.8 EX DG

- 28-70mm F2.8-4 HIGH SPEED ZOOM

- 28-80mm F3.5-5.6 II ASPHERICAL MINI ZOOM MACRO

- 28-105mm F3.8-5.6 UC-III ASPHERICAL IF

- 28-200mm F3.5-5.6 ASPHERICAL MACRO COMPACT HYPERZOOM

- 28-300mm F3.5-6.3 MACRO

- 28-300mm F3.5-6.3 DG Macro

- 55-200mm F4-5.6 DC

- 70-210mm F4-5.6 APO Macro

- 70-300mm F4-5.6 DG Macro

- 135-400mm F4-5.6 APO Aspherical

- 170-500mm F5-6.3 ASPHERICAL RF APO

- 300mm F4 APO TELE MACRO